## Slide 1
Executive Statement
Line 4 output recovered after maintenance, but two unresolved control checks still constrain the Friday capacity release.
Report context
Plant 6 · Line 4 · review window 2026-09-14 through 2026-09-20 · batches L4-260918-A-7741 / B-7742 · owner: Process Engineering.
First-pass yield
96.2%
Unplanned downtime
7.4 h
Chart: Yield by shift
| A | B | C | D
Yield by shift | 94.6 | 95.2 | 96.2 | 95.8
Chart: Critical measurement trend
| 15 | 16 | 17 | 18 | 19 | 20
Critical measurement trend | 95.1 | 95.4 | 95.3 | 95.7 | 94.4 | 95.8
Body Narrative
First-pass yield improved from 94.6% to 96.2% after the valve service. Downtime remains 7.4 hours, above the 6-hour limit. Sample 19 is outside the SPC centerline pattern but inside the product specification; treat this as a process signal for investigation, not a customer defect or capability claim.
Evidence Card
Measurement system remains within the qualified reference range. Sample: 30 parts · method: inline metrology · source: shift B inspection. Verified
Risk Callout
Keep Friday capacity release conditional Await pressure calibration, matched sample 20, and Quality sign-off. A point inside specifications can still warrant a control-chart investigation. Review
Project Card
Complete chamber verification and update the runbook. Owner: Equipment Engineering · due next shift · evidence: paired control lot. Active
Process Flow
Detect
Contain
Verify
Release
Area / identifier | Status | Owner | Due | Evidence
ETCH-08-A / PM-44719 | Calibration open | Equipment Eng. | 09-25 | Pressure offset +2.4 kPa
Line 4 / sample 20 | Matched rerun | Process Eng. | 09-25 | SPC sequence 15–20
Batch L4-260918-B-7742 | Release gated | Quality | 09-26 | Await sign-off; no capability claim