## Slide 1
Body Narrative
Northlight Archive · four collection stores · 1 October 2026 · owner: Conservation · seven-day reversible pilot.
Body Narrative
Relative humidity spans 44.8% to 51.2% across four stores. The south store is above the 50.0% operating target and below the 55.0% stop limit. A one-day observation supports a reversible trial; it does not establish seasonal drift or material damage.
Chart: Humidity by collection store
| North paper store | East textile store | South mixed store | West photography store
Relative humidity | 44.8 | 47.3 | 51.2 | 46.1
Hero Title
Trial the south-store schedule for one week, with daily conservation checks.
South-store humidity
51.2% RH
Lowest versus south-store humidity
44.8% RH → 51.2% RH
Key Takeaway
Decision: run the south-store schedule for seven days. Restore the previous schedule if humidity reaches 55.0% or daily conservation inspection finds any new surface change.
Risk Callout
Trial the south-store schedule for seven days
Restore the prior schedule at 55.0% humidity or any new artifact surface change. Record daily readings and conservation observations before extending the trial.
Trial
Collection store | Humidity | Inspection | Action
North paper store | 44.8% | No change | Maintain
East textile store | 47.3% | No change | Maintain
South mixed store | 51.2% | Review daily | Seven-day trial
West photography store | 46.1% | No change | Maintain
North paper store
East textile store
South mixed store
West photography store