## Slide 1
Body Narrative · Flux recovery rose through the wash and polishing stages, while pressure approached the 2.0 bar watch line at the south header. Chloride remains below the 250 mg/L release criterion. The pressure trace is a prompt to verify the sensor, not proof of membrane damage.
Body Narrative
Bayshore Reuse Plant · 12 process stages, 4 grab samples · shift review 27 Sep 2026 · owner: Water Quality. · Sensor refresh 06:40 · grab sample 06:15 · lab confirmation pending
Chart: Flux recovery by process stage
| 1 Intake | 2 Screen | 3 Carbon | 4 Softener | 5 Train | 6 Wash | 7 Polish | 8 Release
Flux recovery | 63.2 | 63.8 | 64.1 | 64.5 | 65 | 66.1 | 67.4 | 68.4
Chart: Chloride at sampling point
| Intake | Membrane | Polishing | Release
Chloride | 184 | 196 | 207 | 211
Hero Title
Bayshore membrane recovery is improving; keep the release envelope active.
Flux recovery
68.4%
South-header pressure
1.86 bar
Flux before wash / current
63.2% → 68.4%
Key Takeaway
Decision: continue the staged recovery cycle for one shift; release distribution only after the south-header pressure check and the final chloride sample are signed.
Risk Callout
Continue staged recovery for one shift
Hold distribution if south-header pressure exceeds 2.0 bar, final chloride reaches 250 mg/L, or a sensor check fails.
Conditional
Stage | Flux % | Pressure bar | Chloride mg/L | Status
Raw intake | 63.2 | 1.42 | 184 | Baseline
Carbon bed | 64.1 | 1.51 | 191 | Stable
Membrane train | 65 | 1.63 | 198 | Watch
Wash return | 66.1 | 1.72 | 202 | Improving
Polishing pass | 67.4 | 1.81 | 207 | Stable
South header | 68.4 | 1.86 | 211 | Verify sensor
1 Intake
3 Carbon
5 Train
7 Polish
Intake
Membrane
Polishing
Release
Chloride
Release sequence
Screen
feed
pressure
Run
membrane
wash
Verify
pressure
and
chloride
Release d
istributi
on