## Slide 1
Dispatch decision
Verified supply falls toward the 21:00 reserve commitment.
Operating context
Lakeshore cooperative · evening ramp · 17:00–21:00 local · dispatch logs plus balancing desk commitment ledger.
Verified reserve at 20:30
63 MW
Chart: Delivered MW by dispatch resource
| 17:00 | 17:30 | 18:00 | 18:30 | 19:00 | 19:30 | 20:00 | 20:30 | 21:00
Battery | 34 | 32 | 29 | 28 | 25 | 24 | 22 | 21 | 20
Demand response | 18 | 18 | 16 | 16 | 14 | 12 | 10 | 8 | 8
Firm imports | 41 | 40 | 40 | 39 | 37 | 37 | 36 | 34 | 33
Committed reserve versus requirement
63 MW → 70 MW
Supply interpretation
At 20:30 the logged resources total 63 MW against a 70 MW operating reserve requirement. Battery discharge is tapering and the final demand-response block is provisional until telemetry confirms delivery. Imports also trend down across the interval. Keep 7 MW of backup procurement available while dispatch confirms the 21:00 state; these logs describe supply, not delivered customer load.
Dispatch risk / provisional block
Retain the 7 MW backup block until demand-response delivery is verified.
The final response block is provisional and telemetry has not confirmed delivery. Logged supply is 63 MW at 20:30 against the 70 MW requirement; release now would leave the operating reserve under target.
HOLD · telemetry pending
Action / release condition
Next step: confirm demand-response telemetry at 20:45, then release or retain the 7 MW backup block with the balancing desk.
Feeder / contract ID | Verified at 20:30 | Requirement / commitment | Evidence state | Owner
LSH-BAT-04 / inverter INV-77402 | 21 MW | 25 MW scheduled | Telemetry valid; tapering | Storage desk
DR-COMM-209 / block 06 | 8 MW | 15 MW committed | Final interval unconfirmed | Balancing desk
IMP-771-K / North tie | 34 MW | 30 MW minimum | Schedule revised 20:10 | Transmission ops
LSH-RES-70 / operating reserve | 63 MW total | 70 MW required | 7 MW gap | Duty controller
Reserve release path
Validate
meter
quality
Confirm DR
block
delivery
Reconcile
reserve
margin
Release or
retain
backup